## Slide 1: Human-Machine Interfaces for Operating a Blimp
Krebs Matthias, Ledergerber Anton
12.06.2012
Internal supervisors:
Javier Alonso Mora, Konrad Rudin
Notes: Very welcome to the Bsc Thesis Presentation HMI for operating a Blimp

## Slide 2: Motivation
One of skye‘s unique properties:
6 controllable degrees of freedom
Develop a unique HMI and generate Trajectories
To deal with
6 DoF
Camera System
Motor Platform
Control Unit
Accelerometer Gyroscope Magnetoscope Barometer GPS
Communication
Xbee 2.4 GHz Fasst WiFi
Spherical Hull
Filled with Helium
Notes: We‘re sure you all know the Focusproject Skye. We did our Bsc Thesis within this project. (click) Because of skye‘s unique property of 6 controllable degrees of freedom, a good, unique HMI as well as trajectories had to be developed since humans aren‘t used to controll 6 DoF.

## Slide 3: Main tasks
  Develop Control Modes for 6DoF Motion
  Realize HMI
  Generate 3D Trajectories
Notes: These were our main tasks: Control Modes, HMI, Trajectories. Our Presentation is divided into two parts (click), first we will discuss the control modes and the HMI together, and secondly, we will discuss the trajectory generation

## Slide 4: Control Modes
Overview
Direct
Control
Assisted
Control
Half Automatic Control
Testphase
Control
Full Automatic Control
Development of Project skye
Notes: As we started from zero, we couldn‘t start with the most advanced Control Mode for steering. Instead we offered a control mode for each stage of the project, adopted at the hard- and software that was ready. In the following the different modes and their implementations are explained.

## Slide 5: Control Modes
Testphase
8Dof (Angles, Thrust)
Only for testing
Each Motorplatform is controlled seperately
✔
Tested on real
system
Notes: The first step was to control each motor seperately. Skye has 4 maxons for positioning and for brushless motor for generating the thrust. Once we knew that this mode was working, we could be sure that the hardware was ok. (Here we just offered a simple Widget.) (click) (this mode is tested and working) The next thing to attack was the software....

## Slide 6: Control Modes
Direct Control
6Dof (Forces, Moments)
Without Controler
✔
Tested on real
system
Notes: DC Mode is simple a feedforward control for all 6Dof, i. e. the moments and the forces. This mode was useful to test the motor allocation without a (high level controler) Most inuitive is to use a 3d space mouse for that. Therefore a interface to QGC was developed with which the 3d mouse could be attached. (click) this is tested and working on the real system.

## Slide 7: Control Modes
Assisted Control
6Dof (Velocities)
With Controler
✔
Tested on real
System
(in Body
Frame)
Notes: Once the (high level) controler with feedback was working, we didn‘t want to control skye with forces, but with velocities. Beside the space mouse, a GUI for touchinputs was also wished, here you see it in action. (click) The idea was to control the translational velocities in the inertial frame and the rotational velocities in the body frame. Due to problems with the drift of the magnetoscop and the GPS or the state estimation in general, (click) we only tested it with all inputs in the body frame.

## Slide 8: Control Modes
Half Automatic Control
3Dof (Rotational Velocities)
With Trajectory Controler for translational velocities
Pilot control attitude for taking pictures
Notes: In order to ease the job of the pilot 3 Dof should be controled automatically. Before the flight the pilot would set the waypoints on google map and afterwards only control the orientation. This mode was thought best for taking high quality images. Here you see a simulation of this mode(click) (click) only tested in simulation since GPS was not yet working.

## Slide 9: Control Modes
Half Automatic Conrol
✔
Tested in QGC
Simulation

## Slide 10: Control Modes
Full Automatic Control
0 Dof
With Trajectory Controler
With set Target Point
Full Automatic
To appear Video of Simulation
✔
Tested in
Matlab
Simulation

## Slide 11: Path/Trajectory
Body Frame
Inertial Frame

## Slide 12: Approximation/Interpolation

## Slide 13: Spline Degree
Continuity
-cubic
-quartic
-quintic

## Slide 14: Spline Degree, Mot_Alloc
Simulation
C3 Continuity would be best!
Decision
Consider the other effects of the spline degree choice, if quartic has no drawbacks, choose quartic.
C2 seems to be sufficient!

## Slide 15: Parameterization
Motion Law
The decision of parameterization affects the geometry as well as the velocity and acceleration on the trajectory!

## Slide 16: Parameterization
Variants
Equally-distant
Chord-distant
Arc-distant
Centripetal

## Slide 17: Trajectory-Controllers
Trajectories
Precise path tracking
Time equivalence (trajectory tracking)
Low power consumption
Trajectory and Simulation Trace
Trajectory

## Slide 18: Trajectory-Control
Skye
Controllers
3 different approaches: Trajectory Following Pure Pursuit Cross Track
(Lookahead) (Closest Point)
Skye
Pos Control
Trajectory

## Slide 19: Trajectory-Control
Skye
Controllers
3 different approaches: Trajectory Following Pure Pursuit Cross Track
(Lookahead) (Closest Point)
Skye
Vel Control
Trajectory

## Slide 20: Trajectory-Control
Skye
Controllers
3 different approaches: Trajectory Following Pure Pursuit Cross Track
(Lookahead) (Closest Point)
Skye
Pos Control
Trajectory

## Slide 21: Evaluation
Absolute Results
J1: Average Deviation 0.01 m
J2: Average Acceleration 0.1 m/s2
J3: Used Time +/- 5%

## Slide 22: Evaluation
Different Waypoints
Path1
Path2
Path3
„ETH mainbuilding“ „Helix around tree“ „Agil maneuver“

## Slide 23: Evaluation
Performance
J1: Average Deviation
J2: Average Acceleration
J3: Time (always exact)
No wind, centripetal param.
Trajectoy Following
Pure Pursuit
Cross Track
Path1
Path2
Path3
Cubic
Quartic
Quintic

## Slide 24: Evaluation
Performance
J1: Average Deviation
J2: Average Acceleration
J3: Time (85-90%)
Wind 1m/s, centripetal param.
Trajectoy Following
Pure Pursuit
Cross Track
Path1
Path2
Path3
Cubic
Quartic
Quintic

## Slide 25: Evaluation
Performance
J1: Average Deviation
J2: Average Acceleration
J3: Time (85-90%)
Wind 1m/s, centripetal param.
Trajectoy Following
Pure Pursuit
Cross Track
Path1
Path2
Path3
Cubic
Quartic
Quintic

## Slide 26: Evaluation
Performance
J1: Average Deviation
J2: Average Acceleration
J3: Time 85-90%)
Wind 1m/s, centripetal param.
Trajectoy Following
Pure Pursuit
Cross Track
Path1
Path2
Path3
Cubic
Quartic
Quintic

## Slide 27: Evaluation
Robustness
Trajectoy Following
Pure Pursuit
Cross Track
Deviation: 0.010m -> 0.849m 0.014m -> 0.041m 0.006m -> 0.069m
Acceleration: 0.114 -> 0.2389 0.1099 -> 0.1807 0.1088 -> 0.1879

## Slide 28: Evaluation
Correlation
The shorter the way, the higher the accelerations
Either acceleration or deviation will be big
cubic
quartic
quintic
Equally-distant
Chord-distant
Arc-distant
Centripetal

## Slide 29: Conclusion
Working HMI
Choice for Trajectory
Cubic
Centripetal?
CrossTrack?
✔

## Slide 30: >> Backup

## Slide 31: Spline Degree
Motor Allocation
Unrealistic Circuit (20cmx40cmx0cm)
unlike Quadrocopters skye is very inert =>Motion Law prevents it from fast movements
The motor Allocation seems to be able to catch up easily with the dynamics of Skye

## Slide 32: Parameterization
Cubic:

## Slide 33: Evaluation
Correlation
Equally-distant
Chord-distant
Arc-distant
Centripetal
cubic
quartic
quintic

## Slide 34: Evaluation
Correlation
Equally-distant
Chord-distant
Arc-distant
Centripetal
cubic
quartic
quintic
Road only

## Slide 35: Evaluation
Correlation
Equally-distant
Chord-distant
Arc-distant
Centripetal
cubic
quartic
quintic